## Slide 1: Geometry: TLD, T5D, T4D Upgrade4
30 November 2016
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: Line SASE1 & SASE3: Y-plane (vertical)
Angle ‘theta’:
▪ created in CL section
▪ theta_need = -3.65122879e-4 rad (Markus, has to be)
▪ point of transformation from the LA system to the PD system:
at X=0, Y=-2.4386, Z=1994.492 (H.Sinn)
We have:
1) Design:
after CL and at : theta_CL = -3.651232314e-4 rad,
abs(theta_need – theta_CL) = 3.5e-10 rad (relative error = 9.6e-7) - good
2) Upgrade4 (MAD):
at SASE1_Ursprung at SASE3_Ursprung
theta -3.651232314e-4 rad -3.650266017e-4 rad
abs(theta_need – theta) 3.5e-10 rad 9.6e-8 rad
∆Y (from Markus) -2.6e-8 m -2.2e-7 m
SASE3
Linac
CL
theta
SASE1
Y
Z
Angles like in component list.

## Slide 3: Beamline SASE1 & SASE3: X-plane (horizontal)
We have:
1) Design (T4M arc):
phi_our = +0.023007 rad
abs(phi_need – phi_our) = 7.17e-7 rad => smaller for ~0.7 μrad in T4M arc by design
2) Upgrade4 (MAD): at SASE3_Ursprung
phi_MAD = +0.02300700153 rad
abs(phi_need – phi_MAD) = 7.16e-8 rad (~0.7 μrad smaller by design)
X_MAD = -4.808163104 m
∆X= -3.7e-5 m => abs value for ~37 μm smaller
Angle ‘phi’:
▪ phi_need = +0.02300771713 rad (has to be, Markus)
▪ point of transformation from the LA system to the PD system: X=0, Y=-2.4386, Z=1994.492 (H.Sinn)
▪ at SASE3_Ursprung: X = -4.8082 m (Markus)
Linac
CL
Z
X
TL
SASE3
phi
SASE1
T4M

## Slide 4: Beamline TLD
At TLD Dump:
X +1.451329 +1.451349988 2.1e-5 m ≈ 21 μm
Y -9.210116 -9.210120790 4.8e-6 m ≈ 5 μm
Z 2130.518978 2130.518977 1.0e-6 m ≈ 1 μm
theta -0.244710946 -0.244710978 3.2e-8 rad
phi -0.013367998 -0.01336814196 1.4e-7 rad
chi -0.000100351 -0.0001003492143 -
comp_list_8.6.1 Upgrade, Nov 2016 |∆|
new HELP elements

## Slide 5: Line to SASE2: Y-plane (vertical)
Angle ‘theta’:
▪ created in CL section
▪ theta_need = - 3.65122879e-04 (Markus, has to be)
▪ point of transformation from the LA system to the PD system:
at X=0, Y=-2.4386, Z=1994.492 (H.Sinn)
We have:
1) Design:
after CL and at : theta_CL = -3.651232314e-4 rad,
abs(theta_need – theta_CL) = 3.5e-10 rad (relative error = 9.6e-7) => good
2) Upgrade4 (MAD) with new RotSystemTD1 and additionally Rot.Y.Sa2 at Sa2_Ursprung
at SASE2_Ursprung
theta -3.648326915e-4 rad
abs(theta_need – theta) 2.9e-7 rad due to MAD calculations, T1M design is okey
∆Y (from Markus) -9.0e-9 m
SASE2
Linac
CL
theta
Y
Z
T1M

## Slide 6: Beamline to SASE2: X-plane (horizontal)
SASE2
phi
Linac
CL
Z
X
We have:
1) Design of the extraction section (part of TL section + T1M):
phi_our = -0.03989341815 rad
abs(phi_need – phi_our) = 2.37e-6 rad => smaller (abs value) for 2.37 μrad
∆X = +9.23e-5 m at Sa2_Ursprung (5.8015923-5.8015) => larger for 92 μm
2) Upgrade4 (MAD): with new RotSysttemTD1 and additionally Rot.Y.Sa, at SASE2_Ursprung:
phi_MAD = -0.0398957859 rad
abs(phi_need – phi_MAD) = 4e-12 rad (corrected by Rot.Y.Sa2 at Sa2-Ursprung)
∆X = +92 μm (from 5.8015m)
Angle ‘phi’:
▪ phi_need = -0.039895785896 rad (Markus, has to be)
▪ point of transformation from the LA system to the PD system: X=0, Y=-2.4386, Z=1994.492 (H.Sinn)
T1M
TL

## Slide 7: Angles and rotations in MAD
In MAD:
theta – angle of rotation about the global Y-axis (deflection in X-plane)
(= -phi_xls)
phi – elevation angle, i.e. the angle between the reference orbit and
its projection onto (Z,X) plane
(= theta_xls)
psi – roll angle about the local s-axis (= chi_xls)
The angles (theta, phi, psi) are not the Euler angles.
Coordinate transformation In MAD:
YROT - rotates the reference system about the vertical (Y) axis
SROT - rotates the reference system about the longitudinal (S) axis
So:
1) using YROT it is possible to change the angle ‘theta_MAD’ (phi_xls)
2) can not change phi_MAD (theta_xls)